## Slide 1: Sorin HeartLink – Perfusion Systems and Solutions
Christian Chlela
Senior Clinical Expert
Sorin Group

## Slide 2: Steering Perfusion
Assessing the Adequacy of Perfusion:
Goal: To replace respiration and circulation
Intra Operative Assessment:
      Blood gases and hematology
      Circulation flow rates & pressures
      Adherence to standard/best practices and techniques
    Common “Steering” Parameters (Galletti, Berger, Reed, Taylor):
      Flow Index: 2.2 to 2.6 ml/min/m2
      SvO2 > 65%
      PvO2 > 40 mm Hg
      Lactate < 2 mmol/l
    But, M&M problems persist

## Slide 3
0
1
2
3
4
5
6
7
8
9
10
< 18
18
19
20
21
22
23
24
25
26
27
28
> 28
Lowest HCT on CPB
%
Total N/100
% ARF-D
Karkouti et al, Ann Thorac Surg 2003
Cut off
Focal Points in Perfusion
3rd Perfusion Symposium Antalya, TURKEY 2015

## Slide 4
Habib et al, JTCVS 2003
Lowest HCT on CPB is associated to:
Reopening
Bleeding
Perioperative MI
Cardiac arrest
Stroke
Coma
Prolonged ventilation
IABP
Renal failure
MOF
3rd Perfusion Symposium Antalya, TURKEY 2015

## Slide 5: Renal Complications from Cardiopulmonary Bypass
Acute Kidney Injury (AKI) :
  Occurs in 20-30% of patients undergoing CPB
    60 – 100K / yr in the US
    Estimate $1 billion to treat
  If dialysis is required:
    Up to 50% mortality
    Patients remain dialysis dependent

## Slide 6: Common Perfusion Steering Parameters
Common “Steering” Parameters (Galletti, Berger, Reed, Taylor):
  Flow Index: 2.2 to 2.6 ml/min/m2
  SvO2 > 65%
  PvO2 > 40 mm Hg
  Lactate < 2 mmol/l
BSA only
Full systemic parameters: no regional information
Result of extended anaerobic metabolism
Acute Anemia:
Reduced viscosity
Increased cardiac output
Perfusion Anemia:
Pump flow based on BSA
3rd Perfusion Symposium Antalya, TURKEY 2015

## Slide 7: Reducing Kidney Injury Associated with CBP
Cited by 32 articles available in literature
Test premise that lowest Hct on CPB is risk factor for renal failure:
1048 pt study: Lowest Hct, Lowest O2 delivery, Qb, transfusions
Best predictor of ARF/AKI was the lowest O2 delivery
High hemodilution is a risk factor for ARF/AKI:
  Reduced by increasing O2 delivery and pump flow
  Critical O2 delivery of 272 ml/min/m2: aerobic/anaerobic threshold
Kidney is sensitive to low O2 delivery:
  Both O2 content and flow rate
3rd Perfusion Symposium Antalya, TURKEY 2015

## Slide 8: Acute Renal Failure and DO2
Chart: Renal Replacement- Acute Renal Failure Occurrence (%) N =1048 pts
| High HCT High DO2 | Low HCT High DO2 | High HCT Low DO2 | Low HCT Low DO2
Renal replacement- Acute renal failure (%) | 0.011 | 0.019 | 0.044 | 0.062
Source: Ranucci et al, Oxygen Delivery During Cardiopulmonary Bypass and Acute Renal Failure After Coronary Operations,Ann Thorac Surg 2005,; 80; 2213-2220

## Slide 9: Nadir DO2 Above Threshold Effectively Guides Therapy de Somer, et al. Time for GDP?
359 Cardiac surgery patients
DO2 “modifiable risk factor” in preventing AKI
Nadir DO2 above threshold effective guide to therapy
Nadir DO2/VCO2 further guides management

## Slide 10: Factors and Management of AKI
Intraoperative Factors:
CPB-SIRS response
Emboli from CPB
Hemodynamic alterations
Intraoperative Strategies:
Min hemoglobin/Hct:
  7.0 g/dl / 21
MAP 50 – 70 mmHg
Flows: 2.2 – 2.5
Minimize CPB time

## Slide 11: Standardized perfusion approach - Pump flow based on BSA
Patients with same BSA, but very different physical characteristics may receive the same pump flow
They might have different oxygen supply needs
Hct is not considered
While normally cardiac output adapts to Hct (e.g it increases in case of anemia)

## Slide 12: Respiration and Metabolic State

## Slide 13
Respiration and Metabolic State

## Slide 14
Respiration and Metabolic State

## Slide 15
Respiration and Metabolic State

## Slide 16
Respiration and Metabolic State

## Slide 17: GDP MonitorTM: Oxygen Delivery DO2
DO2i> 262 mL/min/m2
DO2i
Real-time assessment of adequacy of flow and hematocrit
DO2 is the amount of oxygen delivered to the whole body from the lungs/oxygenator.
Indexed DO2
3rd Perfusion Symposium Antalya, TURKEY 2015

## Slide 18: GDP MonitorTM: Carbon Dioxide Production VCO2
VCO2 is the amount of carbon dioxide produced by the tissues, measured as the amount of carbon dioxide given off by the oxygenator :
Capnograph
DO2i/VCO2i> 5
VCO2
Predictor of lactate metabolism
3rd Perfusion Symposium Antalya, TURKEY 2015

## Slide 19: GDP Monitor TM allows to monitor real time the key patient metabolic parameters during CPB

## Slide 20: Effect of GDP on kidney injury
Chart: 
| Control | GDP | Control tx | GDP tx
New AKI % | 25 | 9 | 45 | 4
Goal Directed Perfusion (GDP)
  Reduces post operative creatinine increase
  Reduced AKI rate from 25 % to 9 %
Low hemoglobin patients
  Significantly reduces creatinine increase in patients that require a transfusion
  Reduces new AKI in small, anemic patients

## Slide 21: Effect of Sorin Inspire and Goal Directed Perfusion (GDP) on PRBC Transfusion
Chart: PRBC Utilization Rate
| 2013 Q3 | 2013 Q4 | 2014 Q1 | 2014 Q2 | 2014 Q3
PRBC % | 46.2 | 32.1 | 28.7 | 25.7 | 23
Column1
Column2
Baseline PRBC Transfusion Rate
  46%
  Volume mean 2.8 units
End of August 2014 PRBC Rate
  23%
  Volume mean 0.63 units
50% reduction in frequency of PRBC
77% reduction in volume of PRBC units

## Slide 22: Sorin HeartLink One System, Many Solutions

## Slide 23
THANK YOU FOR YOUR TIME.
Questions ?
3rd Perfusion Symposium Antalya, TURKEY 2015